## Slide 1: Wired, Wireless and Optical Systems
Text: Communication Systems Principles using MATLAB®
Text, drawings and images copyright © John Wiley & Sons 2018

## Slide 2: Chapter Aims
Learn about wired systems – such as Ethernet, and how voltages encode data.
Learn about wireless systems – how radio modulation works.
Learn about fiber optic systems – how laser light encodes digital information within an optical fiber.
Some basic design principles for the above, such as how much power is required for a certain performance level.

## Slide 3: Fourier Series
Any waveform which is periodic (ie repeats a basic template) can be decomposed
  A sum of weighted sine waves, plus
  A sum of weighted cosine waves, plus
  A constant or DC offset
The DC offset is a special case of cosine with frequency = 0
Analysis: work out the weighting coefficients.
Synthesis: sum the weighted waves so as to approximate the original.
Extend this: sine and cosine expressed as one sine (or cosine) but with a certain amplitude and phase shift.
Usually only interested in the magnitude, which is square root of sine squared plus cosine squared.

## Slide 4: Fourier Transform
Similar concept but now have a measured signal. A finite-duration measurement time.
Two-component wave: can we determine the frequencies present?
Expect two frequencies, but widens to become a `sinc’ function.
These sidelobes are due to a finite measurement time.
Smooth the wave using a taper or Window function.
Gives smoother spectrum but wider range, ie uncertainty.

## Slide 5: Spectrum Analyzer
Measures frequency content of a signal, eg radio signal.
Basically a Fourier Transform, but does this in a different way.
Sweeps the test frequency, mixes it with incoming frequency, detects the result and plots it as the spectrum.

## Slide 6: Spectrum Analyzer
Example with sine oscillator input.
Notes: power in dBm, frequency MHz, noise floor, resolution/width of spectral peak
Resolution bandwidth = width of the filter
Video bandwidth = averaging time.

## Slide 7: Transmission Modes
Important distinction:
  Baseband – where we send basically a voltage or light pulse. Typically wired local area networks and fiber optic.
  Passband – where the information/data is modulated onto a carrier. Typically wireless but could be wired.

## Slide 8: Cables and Pulses
Wires – shielded and twisted pair.
Single-ended or unbalanced vs Differential or balanced.

## Slide 9: Pulse Transmission
Bandwidth of cable not infinite, lowpass filters pulse.
So pulse spreads out.
Other effects too, inductance and capacitance.
Pure pulses shown.
Pulse rings and ends at A.
Peak pulse magnitude at B.
Start new pulse at C.
Result: more pulses, more data sent in a given time.

## Slide 10: Sinc function
Pure pulse but with limited bandwidth.
Equation is
is pulse zero-crossing interval.
Idea extended to raised-cosine filter to “pre-shape” pulses for a given channel.

## Slide 11: Line Codes
Baseband
Why is encoding necessary? To maintain synchronism.
Sender clock may drift; receiver may drift. May have same frequency but different phase.
Long run of the same level looks like constant DC, so no timing information.
Possible to send more than one bit at a time.

## Slide 12: Line Codes
Rules for each type of encoding.
Main aim: to give some transitions for receiver to see & lock onto.
Other techniques used in tandem, eg 4B5B to add sufficient transitions.
Another issue is spectrum: cable acts like an antenna, radiates out signal and causes interference.
Some techniques also used in magnetic recording.

## Slide 13: Pulse Reflection
What happens when a pulse reaches the end of a transmission line? Might bounce back.
This reflection interferes with the next pulses travelling to the receiver. Result is scrambled waveforms.
Length may be long with respect to pulse propagation time.
Terminating impedance: radio frequency often Ethernet

## Slide 14: Pulse Reflection
If end is open-circuit, impedance is infinite.
Reflection coefficient is
Note forward pulse.
Note reflected pulse, same amplitude and reflected in-phase.
Then the summation of these is what is seen at the source.

## Slide 15: Pulse Reflection
If end is short-circuited, impedance is zero.
Reflection coefficient is
Note forward pulse.
Note reflected pulse, reversed in phase and same amplitude.
Then the summation of these is what is seen at the source.

## Slide 16: Pulse Reflection
If end impedance is
Reflection coefficient is
Note forward pulse.
Note reflected pulse, reversed in phase, reduced in amplitude.
Then the summation of these is what is seen at the source.

## Slide 17: Pulse Reflection
If end impedance is
Reflection coefficient is
Note forward pulse.
Note reflected pulse. In-phase but smaller.
Then the summation of these is what is seen at the source.

## Slide 18: Pulse Reflection – Finally
If end impedance is
Reflection coefficient is
Note forward pulse.
There is no reflection.
So no distortion of forward-travelling pulse.
All power absorbed by the load; impedance-matched.

## Slide 19: Wave Reflection
Extend idea from single pulse to a continuous sinusoidal waveform.
Same ideas of reflection, impedance, reflection coefficient apply.
Phase delay due to distance is radians per unit length
Wave equation is

## Slide 20: Wave Reflection
Extend idea from single pulse to a continuous sinusoidal waveform.
Note horizontal axis is distance, not time.
Reflection with phase of zero shown.

## Slide 21: Wave Reflection
Extend idea from single pulse to a continuous sinusoidal waveform.
Note horizontal axis is distance, not time.
Reflection with phase of 180 degrees shown.

## Slide 22: Wave Reflection
Extend idea from single pulse to a continuous sinusoidal waveform.
Note horizontal axis is distance, not time.
Reflection with phase of zero and gain 0.5
Looking at envelope (summation), have VSWR: Voltage Standing Wave Ratio

## Slide 23: Radio and Wireless
Radio signals useful if we don’t want to be stuck in one place.
Very wide range of frequencies possible.
Which frequency works best depends on the application:
  How far you want the signal to go (next door? into space?)
  How large an antenna can you cope with?
  How much data do you want to transmit (bits per second).
  Is the sender or receiver moving? Is it in the air, underwater?
Note also fiber optic bandwidth, just below visible light.
Frequency versus wavelength
  Lower frequency … longer wavelength
  Shorter wavelength … higher frequency.

## Slide 24: Radio and Wireless
Common radio/wireless bands
Extra low frequencies – maybe if you have a need to talk to a submarine.
Low and very low frequencies – need really big antennas.
Medium frequency – not difficult to receive, but over short range (think car radios)
High frequency – can bounce off the ionosphere. Used a lot before there were satellites or undersea fiber cables.
Very high frequency – emergency radios, shorter range and less interference.
Ultra high frequency – mobile cell phones, WiFi. Very short wavelength so small antenna. Such high frequencies are difficult to deal with. Problem: won’t travel through buildings or people that well.
Super high – satellite and point-to-point. But watch out for clouds.
General principle: lower frequencies radiate out equally, but higher frequencies tend to travel in a straight line.

## Slide 25: Radio Horizon
If you need to transmit a long distance, curvature of the earth may be a problem.
is the height of the antenna tower (transmitter or receiver, or both)
is the distance you want to send over
Using geometry, can derive an approximation:
Height needs to be in meters, distance in km.
Example: 4 m tower, can transmit about 8 km as an approximation.

## Slide 26: Radio Reflection
Radio waves are electromagnetic, so have reflections.
Distance of direct wave is different to indirect path
By the time the direct wave arrives at the receiver, the reflected wave might have travelled further, so a phase difference.
Might also be a phase change at point of reflection.

## Slide 27: Radio Reflection
Suppose delayed waveform is not actually delayed.
Not a problem, they reinforce each other.
This is actually good.
Step through following to show changes…

## Slide 28: Radio Reflection
Suppose delayed waveform is delayed a little. Takes longer to get there.
They add, but result is not as large.
Not quite as good.

## Slide 29: Radio Reflection
Delay a little more.
Result is getting smaller.

## Slide 30: Radio Reflection
Delay such that they are out-of-phase.
They add… or actually cancel.
No signal at all at receiver.

## Slide 31: Radio Reflection
Result: using some geometry, the path difference is then
The phase difference, which governs the addition/subtraction, is
Shows that a change in antenna heights can affect the phase.
Also shows that physical distance with respect to the radio wavelength is important.
If path difference is much less than the wavelength then there may not be a problem.
On the other hand, small wavelengths may mean big problems.

## Slide 32: Radio Diffraction
Drop a stone in a pond. Creates ripples.
Similar idea when radio wave encounters an obstacle (building, tree, mountain)
So some areas may be “dark” and not receive much signal.

## Slide 33: Radio Diffraction
Consider “knife-edge” diffraction.
Obstacle close to direct path, but not directly in path.
Partial cancellation may result if diffracted received wave out-of-phase with direct path wave.
Occurs when

## Slide 34: Moving Sender or Receiver
Results in Doppler Effect.
Changes apparent frequency of radio wave.
Apparent frequency

## Slide 35: Radio Antennas
Many, many types. Dipole is the most fundamental.
Can act as send or receive antenna.
Key idea: the two “arms” act as a resonant circuit with reflections.
This maximizes the standing wave on the arms themselves.

## Slide 36: Radio Antennas
Resulting dipole pattern, as if viewed from above.
Dipole arms along zero degree axis.
Maximum power out (or maximum sensitivity) perpendicular to this.
Minimum (theoretically zero) power (or sensitivity) along dipole axis.

## Slide 37: Radio Antennas
Extend dipole to a Yagi.
Directors and reflector.
Numerous variations on the basic theme.

## Slide 38: Radio Reception
Signal (voice, data) occupies baseband. But radio signal is much higher in frequency.
Problem: how to translate baseband up when transmitting?
Problem: how to translate radio back to baseband when receiving?
Need frequency translation.

## Slide 39: Radio Reception
Usual method is to use a mixer.
Multiplies radio frequency (RF) by an oscillator of similar (not identical) frequency.
Then removes high-frequency component with a filter.

## Slide 40: Radio Reception
Why does mixing use multiplication?
Multiply these fairly close frequencies.
You can see that the product contains a higher frequency as well as a lower frequency.
Average out the higher frequency to see the lower one.

## Slide 41: Radio Reception
Mixing uses the Local Oscillator (LO).
May be shown that the sum and difference frequencies result.
The Intermediate Frequency (IF) is the difference (lower) frequency.

## Slide 42: Radio Noise
Other transmitters present.
Other devices may produce interfering signals.
Background noise.
Limit of resolution of receiver.

## Slide 43: Optical Transmission
Optical fibers are capable of very fast data transmission. Was not always the case.
Requires matching source (Laser) with cable (fiber) with receiver (detector).
Laser source is a Laser Diode. Relies on standing waves within a cavity.
Laser may required optical stabilization and/or temperature control.
Multiple narrow emission lines (depends on type of laser).
Optical fiber may be single-mode or multi-mode.

## Slide 44: Optical Transmission
Single-mode much smaller than multimode.
Containment of light within a fiber requires both a core and a cladding.
Multimode optical fiber may be step-index or graded index.
The cladding is not just for strength, it is required to ensure light propagation

## Slide 45: Optical Transmission
Single-mode much smaller than multimode.
Containment of light within a fiber requires both a core and a cladding.
Multimode optical fiber may be step-index or graded index.
Refraction is critical to fiber optics.

## Slide 46: Optical Transmission
The cladding is not just for strength, it is required to ensure light propagation
Requires total internal reflection to keep light within core.

## Slide 47: Optical Transmission
Test optical fibers using Optical Time Domain Reflectometry (OTDR)
Can tell connector loss, fiber signal loss, fiber breakages. Bends also cause loss of signal.

## Slide 48: Chapter Summary – Key Points
Digital pulse transmission: line coding, synchronization and scrambling.
Principles of radio frequency: change in frequency by mixing; the definition of RF bands and their use in practice.
Transmission lines: reflections and standing waves.
Propagation of radio frequencies and basic principles of antennas.
Optical communications: light sources and detection, principles of optical fibers, and design and test of fiber links.